深圳市光越光电子有限公司

SHENZHEN GUANGGUE INDUSTRIAL DEVELOPMENT CO.,LTD.

承 认 书

# SPECIFICATION FOR APPROVAL

客    户CUSTOMER

样品编号 SPEC NO

产品型号 PART NO                  3MM-SYGC/1618

产品规格 MODEL                 白发普绿

日    期  DATE

客户确认结果及意见CUSTOMER CONFIRMATION OUTCOME OPINION：

| 客户确认： 合格 不合格 | 2014年 10 月 21 日 |
| --- | --- |
| 客户意见： |

承认签名APPROVED SIGN-ATURES

| 核 准 PREPARED BY |  | 核 对 CHECKED BY |  | 承 认 ACCEPT |  |
| --- | --- | --- | --- | --- | --- |

核  准：                   核  对 ：                填  表：

PREPARED BY：                  CHECKED BY：                   APPROVED BY：

尺寸图： Item Materials Resin Epoxy Lens Color Colorless

#### SPECIFICATION

Absolute Maximum Rating	(Ta = 25℃)

| Items | Symbol | Absolute maximum Rating | Unit |
| --- | --- | --- | --- |
| Forward Current | IF | 30 | mA |
| Peak Forward Current＊ | IFP | 100 | mA |
| Reverse Voltage | VR | 5 | V |
| Power Dissipation | PD | 120 | mW |
| Electyostatic discharge | ESD | 2000 | V |
| Operation Temperature | Topr | -30 ~ +85 | ℃ |
| Storage Temperature | Tstg | -40 ~ +100 | ℃ |
| Lead Soldering Temperature＊ | Tsol | Max 260(C for 5 sec Max |

＊IFP Conditions: Pulse Width≤10msec

＊Tsol Conditions:3mm from the base of the epoxy bulb

Initial Electrical/Optical Characteristics	（Ta=25℃）

| 项目 | 符号 | 条件值 | Min. | Typ. | Max. | Unit |
| --- | --- | --- | --- | --- | --- | --- |
| 顺向电压 | VF | IF = 20mA | 2.0 | --- | 2.2 | V |
| 反向电流 | IR | VR = 5V | --- | --- | 10 | μΑ |
| 波长 | Wd | IF=20mA | 560 | 565 | 570 | nm |
| 亮度 | Iv | IF=20mA | 50 | ------ | 80 | mcd |
| 视角 | 2θ( | IF =20mA | --- | 25 | --- | deg |

Notes:

*One normal delivery will include all ranks listed above.

The quantity ratio of  the ranks is decided by LaiSuo

Measurement Uncertainty of the Luminous intensity : ±15%

Measurement Uncertainty of the Dominant Wavelength : ±1.0nm

#### RELIABILITY

Test Items And Results

| Type | Test Item | REF. Standard | Test Condition | Note | Number of Damaged |
| --- | --- | --- | --- | --- | --- |
| Environmental Sequence | Temperature Cycle | JIS C 7021 (1977)A-4 | -40℃( 25℃( 100℃( 25℃ 30mins, 5mins, 30mins, 5mins | 100 cycles | 0 / 100 |
|  | Thermal Shock | MIL-STD-107D | -40℃( 100℃ 15mins, 15mins | 100 cycles | 0 / 100 |
|  | High Humidity Heat Cycle | JIS C 7021 (1977)A-5 | 30℃( 65℃ 90%RH 24hrs/1cycle | 10 cycles | 0 / 100 |
|  | High Temperature Storage | JIS C 7021 (1977)B-10 | Ta = 100℃ | 1000hrs | 0 / 100 |
|  | Humidity Heat Storage | JIS C 7021 (1977)B-11 | Ta = 60℃ RH = 90% | 1000hrs | 0 / 100 |
|  | Low Temperature Storage | JIS C 7021 (1977)B-12 | Ta = -40℃ | 1000hrs | 0 / 100 |
| Operation Sequence | Life Test | JIS C 7035 (1985) | Ta = 25℃ IF = 30mA | 1000hrs | 0 / 100 |
|  | High Humidity Heat Life Test | * | 60℃ RH=90% IF = 20mA | 500hrs | 0 / 100 |
|  | Low Temperature Life Test | * | Ta = -40℃ IF = 20mA | 1000hrs | 0 / 100 |
| Destructive Sequence | Resistance to Soldering Heat | JIS C 7021 (1977)A-11 | Tsol = 260±5℃ , 10sec (3mm from the base of the epoxy bulb) | 1 time | 0 / 20 |
|  | Solderability | JIS C 7021 (1977)A-2 | Tsol = 235±5℃ , 5sec (using flux) | 1 time (over 95%) | 0 / 20 |
|  | Lead Pull/Bend Test | JIS C 7021 (1977)A-11 | Load 2.5N (0.25kgf) 0°( 90°( 0° bend 3 times | No noticeable damage | 0 / 20 |

*Refer to reliabiltiy test standard specification for in this line.

# Text boxes

注意事项

# （一）LED焊接条件

（1）烙铁焊接：烙铁（最高30W）尖端温度不超过300℃；烙铁必需接地，静电不能超范围；焊接时间不超过3秒；焊接位置至少离胶体3毫米。

（2）浸焊：浸焊最高温度260℃；浸焊时间不超过5秒；浸焊位置至少离胶体3毫米。

# （二）引脚成形方法

（1）必需离胶体2毫米才能折弯支架。

（2）支架成形必须用夹具或由专业人员来完成。

（3）支架成形必须在焊接前完成。

（4）支架成形需保证引脚和间距与线路板上一致。

# （三）LED安装方法

（1）注意各类器件外线的排列，以防极性装错。器件不可与发热元件靠得太近，工作条件不要超过其规定的极限。

（2）务必不要在引脚变形的情况下安装LED。

（3）当决定在孔中安装时，计算好面孔及线路板上孔距的尺寸和公差以免支架受过度的压力。

（4）安装LED时，建议用导套定位。

（5）在焊接温度回到正常以前，必须避免使LED受到任何的震动或外力。

# （四）清洗

当用化学品清洗胶体时必须特别小心，因为有些化学品对胶体表面有损伤并引起褪色如三氯乙烯、丙酮等。可用乙醇擦拭、浸渍，时间在常温下不超过3分钟。